ATTENUATION RELATIONSHIPS

The enclosed three Attachments summarize a number of attenuation relationships currently available to estimate earthquake ground motions in Western North America (WNA), Eastern North America (ENA), and for earthquakes occurring on subduction zones.

These attenuation relationships provide estimates of earthquake ground motions at "rock sites".

- Attachment 1 pertains to earthquake ground motions in Western North America (WNA).

- Attachment 2 pertains to earthquake ground motions in Eastern North America (ENA).

- Attachment 3 pertains to earthquake ground motions generated by earthquakes occurring in subduction zones.

Note: This document was prepared for distribution at the Refresher Course on "Seismic Analysis and Retrofitting of Lifeline Buildings in Delhi, India", held at the Auditorium of the Delhi Secretariat Building on May 26, 2005.

ATTACHMENT 1

ATTENUATION RELATIONSHIPS FOR MOTIONS

IN WESTERN NORTH AMERICA (WNA)

The attenuation relationships derived by Abrahamson and Silva (1997), by Boore, Joyner and Fumal (1997), by Campbell (1997), by Idriss (2002), and by Sadigh et al (1997), are summarized in this Attachment.

1.1 ATTENUATION RELATIONSHIPS DERIVED BY ABRAHAMSON & SILVA (1997)

The functional form adopted by Abrahamson and Silva for spectral ordinates at rock sites is the following:

|  | [1-1] |
| --- | --- |

in which,  is the median spectral acceleration in g (5% damping), or peak ground acceleration (pga), in g's,  is moment magnitude,  is the closest distance to the rupture plane in km,  is the fault type (1 for reverse, 0.5 for reverse/oblique, and 0 otherwise), and  is a dummy variable for sites located on the hanging wall (1 for sites over the hanging wall, 0 otherwise).  The function  is given by.

| for for | [1-2] |
| --- | --- |

Note that  in Eq. [1-2}.

The function  is described below:

| for for for | [1-3] |
| --- | --- |

The function  is assumed to consist of the product of the following two functions, namely:

|  | [1-4] |
| --- | --- |

The function  is evaluated as follows:

| for for for | [1-5] |
| --- | --- |

The function  is given by:

| for for for for for | [1-6] |
| --- | --- |

The standard error terms are given by the following equations:

| for for for | [1-7] |
| --- | --- |

Values of the coefficients , and  are listed in Table 1-1 for periods ranging from  = 0.01 sec (representing zpa) to  = 5 sec.  Values of the coefficients  and  are listed in Table 1-2 for the same periods.

Table 1-1 Coefficients for the Median Spectral Ordinates Using Equations Derived by Abrahamson and Silva (1997)

| Period |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.01 | 5.60 | 1.640 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.417 | -0.230 | 0.0000 |
| 0.02 | 5.60 | 1.640 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.417 | -0.230 | 0.0000 |
| 0.03 | 5.60 | 1.690 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.470 | -0.230 | 0.0143 |
| 0.04 | 5.60 | 1.780 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.555 | -0.251 | 0.0245 |
| 0.05 | 5.60 | 1.870 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.620 | -0.267 | 0.0280 |
| 0.06 | 5.60 | 1.940 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.665 | -0.280 | 0.0300 |
| 0.075 | 5.58 | 2.037 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.628 | -0.280 | 0.0300 |
| 0.09 | 5.54 | 2.100 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.609 | -0.280 | 0.0300 |
| 0.1 | 5.50 | 2.160 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.598 | -0.280 | 0.0280 |
| 0.12 | 5.39 | 2.272 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.591 | -0.280 | 0.0180 |
| 0.15 | 5.27 | 2.407 | 0.512 | -1.1450 | -0.144 | 0.610 | 0.260 | 0.370 | -0.577 | -0.280 | 0.0050 |
| 0.17 | 5.19 | 2.430 | 0.512 | -1.1350 | -0.144 | 0.610 | 0.260 | 0.370 | -0.522 | -0.265 | -0.0040 |
| 0.2 | 5.10 | 2.406 | 0.512 | -1.1150 | -0.144 | 0.610 | 0.260 | 0.370 | -0.445 | -0.245 | -0.0138 |
| 0.24 | 4.97 | 2.293 | 0.512 | -1.0790 | -0.144 | 0.610 | 0.232 | 0.370 | -0.350 | -0.223 | -0.0238 |
| 0.3 | 4.80 | 2.114 | 0.512 | -1.0350 | -0.144 | 0.610 | 0.198 | 0.370 | -0.219 | -0.195 | -0.0360 |
| 0.36 | 4.62 | 1.955 | 0.512 | -1.0052 | -0.144 | 0.610 | 0.170 | 0.370 | -0.123 | -0.173 | -0.0460 |
| 0.4 | 4.52 | 1.860 | 0.512 | -0.9880 | -0.144 | 0.610 | 0.154 | 0.370 | -0.065 | -0.160 | -0.0518 |
| 0.46 | 4.38 | 1.717 | 0.512 | -0.9652 | -0.144 | 0.592 | 0.132 | 0.370 | 0.020 | -0.136 | -0.0594 |
| 0.5 | 4.30 | 1.615 | 0.512 | -0.9515 | -0.144 | 0.581 | 0.119 | 0.370 | 0.085 | -0.121 | -0.0635 |
| 0.6 | 4.12 | 1.428 | 0.512 | -0.9218 | -0.144 | 0.557 | 0.091 | 0.370 | 0.194 | -0.089 | -0.0740 |
| 0.75 | 3.90 | 1.160 | 0.512 | -0.8852 | -0.144 | 0.528 | 0.057 | 0.331 | 0.320 | -0.050 | -0.0862 |
| 0.85 | 3.81 | 1.020 | 0.512 | -0.8648 | -0.144 | 0.512 | 0.038 | 0.309 | 0.370 | -0.028 | -0.0927 |
| 1 | 3.70 | 0.828 | 0.512 | -0.8383 | -0.144 | 0.490 | 0.013 | 0.281 | 0.423 | 0.000 | -0.1020 |
| 1.5 | 3.55 | 0.260 | 0.512 | -0.7721 | -0.144 | 0.438 | -0.049 | 0.210 | 0.600 | 0.040 | -0.1200 |
| 2 | 3.50 | -0.150 | 0.512 | -0.7250 | -0.144 | 0.400 | -0.094 | 0.160 | 0.610 | 0.040 | -0.1400 |
| 3 | 3.50 | -0.690 | 0.512 | -0.7250 | -0.144 | 0.400 | -0.156 | 0.089 | 0.630 | 0.040 | -0.1726 |
| 4 | 3.50 | -1.130 | 0.512 | -0.7250 | -0.144 | 0.400 | -0.200 | 0.039 | 0.640 | 0.040 | -0.1956 |
| 5 | 3.50 | -1.460 | 0.512 | -0.7250 | -0.144 | 0.400 | -0.200 | 0.000 | 0.664 | 0.040 | -0.2150 |

The coefficients  = 0.17,  = 6.4,  = 0.03, and  = 2 for all periods.

Table 1-2 Coefficients for Standard Error Terms Using Equations Derived by Abrahamson and Silva (1997)

| Period - sec |  |  |
| --- | --- | --- |
| 0.01 | 0.70 | 0.135 |
| 0.02 | 0.70 | 0.135 |
| 0.03 | 0.70 | 0.135 |
| 0.04 | 0.71 | 0.135 |
| 0.05 | 0.71 | 0.135 |
| 0.06 | 0.72 | 0.135 |
| 0.075 | 0.73 | 0.135 |
| 0.09 | 0.74 | 0.135 |
| 0.1 | 0.74 | 0.135 |
| 0.12 | 0.75 | 0.135 |
| 0.15 | 0.75 | 0.135 |
| 0.17 | 0.76 | 0.135 |
| 0.2 | 0.77 | 0.135 |
| 0.24 | 0.77 | 0.135 |
| 0.3 | 0.78 | 0.135 |
| 0.36 | 0.79 | 0.135 |
| 0.4 | 0.79 | 0.135 |
| 0.46 | 0.80 | 0.132 |
| 0.5 | 0.80 | 0.130 |
| 0.6 | 0.81 | 0.127 |
| 0.75 | 0.81 | 0.123 |
| 0.85 | 0.82 | 0.121 |
| 1 | 0.83 | 0.118 |
| 1.5 | 0.84 | 0.110 |
| 2 | 0.85 | 0.105 |
| 3 | 0.87 | 0.097 |
| 4 | 0.88 | 0.092 |
| 5 | 0.89 | 0.087 |

1.2 ATTENUATION RELATIONSHIPS DERIVED BY BOORE, JOYNER AND FUMAL (1997)

The following equation was derived by Boore et al for spectral ordinates at rock sites:

|  | [1-8] |
| --- | --- |

|  | [1-9] |
| --- | --- |

The variable y is spectral acceleration (5% damping) in g's;  is moment magnitude,  is the average shear wave velocity (in m/sec)in the upper 30 m of the profile under consideration,  is reference shear wave velocity (in m/sec), and  is the closest horizontal distance (in km) from the site to the surface projection of the source.  Values of the coefficients  and  (in km) are listed in Table 1-3.  Also listed in Table 1-3 are the values of the standard error terms.

Table 1-3

Coefficients Derived by Boore, Fumal and Joyner (1997)

| Period |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | -0.313 | -0.117 | -0.242 | 0.527 | 0.000 | -0.778 | -0.371 | 1396 | 5.57 | 0.520 |
| 0.10 | 1.006 | 1.087 | 1.059 | 0.753 | -0.226 | -0.934 | -0.212 | 1112 | 6.27 | 0.479 |
| 0.11 | 1.072 | 1.164 | 1.130 | 0.732 | -0.230 | -0.937 | -0.211 | 1291 | 6.65 | 0.481 |
| 0.12 | 1.109 | 1.215 | 1.174 | 0.721 | -0.233 | -0.939 | -0.215 | 1452 | 6.91 | 0.485 |
| 0.13 | 1.128 | 1.246 | 1.200 | 0.711 | -0.233 | -0.939 | -0.221 | 1596 | 7.08 | 0.486 |
| 0.14 | 1.135 | 1.261 | 1.208 | 0.707 | -0.230 | -0.938 | -0.228 | 1718 | 7.18 | 0.489 |
| 0.15 | 1.128 | 1.264 | 1.204 | 0.702 | -0.228 | -0.937 | -0.238 | 1820 | 7.23 | 0.492 |
| 0.16 | 1.112 | 1.257 | 1.192 | 0.702 | -0.226 | -0.935 | -0.248 | 1910 | 7.24 | 0.495 |
| 0.17 | 1.090 | 1.242 | 1.173 | 0.702 | -0.221 | -0.933 | -0.258 | 1977 | 7.21 | 0.497 |
| 0.18 | 1.063 | 1.222 | 1.151 | 0.705 | -0.216 | -0.930 | -0.270 | 2037 | 7.16 | 0.499 |
| 0.19 | 1.032 | 1.198 | 1.122 | 0.709 | -0.212 | -0.927 | -0.281 | 2080 | 7.10 | 0.501 |
| 0.20 | 0.999 | 1.170 | 1.089 | 0.711 | -0.207 | -0.924 | -0.292 | 2118 | 7.02 | 0.502 |
| 0.22 | 0.925 | 1.104 | 1.019 | 0.721 | -0.198 | -0.918 | -0.315 | 2158 | 6.83 | 0.508 |
| 0.24 | 0.847 | 1.033 | 0.941 | 0.732 | -0.189 | -0.912 | -0.338 | 2178 | 6.62 | 0.511 |
| 0.26 | 0.764 | 0.958 | 0.861 | 0.744 | -0.180 | -0.906 | -0.360 | 2173 | 6.39 | 0.514 |
| 0.28 | 0.681 | 0.881 | 0.780 | 0.758 | -0.168 | -0.899 | -0.381 | 2158 | 6.17 | 0.518 |
| 0.30 | 0.598 | 0.803 | 0.700 | 0.769 | -0.161 | -0.893 | -0.401 | 2133 | 5.94 | 0.522 |
| 0.32 | 0.518 | 0.725 | 0.619 | 0.783 | -0.152 | -0.888 | -0.420 | 2104 | 5.72 | 0.525 |
| 0.34 | 0.439 | 0.648 | 0.540 | 0.794 | -0.143 | -0.882 | -0.438 | 2070 | 5.50 | 0.530 |
| 0.36 | 0.361 | 0.570 | 0.462 | 0.806 | -0.136 | -0.877 | -0.456 | 2032 | 5.30 | 0.532 |
| 0.38 | 0.286 | 0.495 | 0.385 | 0.820 | -0.127 | -0.872 | -0.472 | 1995 | 5.10 | 0.536 |
| 0.40 | 0.212 | 0.423 | 0.311 | 0.831 | -0.120 | -0.867 | -0.487 | 1954 | 4.91 | 0.538 |
| 0.42 | 0.140 | 0.352 | 0.239 | 0.840 | -0.113 | -0.862 | -0.502 | 1919 | 4.74 | 0.542 |
| 0.44 | 0.073 | 0.282 | 0.169 | 0.852 | -0.108 | -0.858 | -0.516 | 1884 | 4.57 | 0.545 |
| 0.46 | 0.005 | 0.217 | 0.102 | 0.863 | -0.101 | -0.854 | -0.529 | 1849 | 4.41 | 0.549 |
| 0.48 | -0.058 | 0.151 | 0.036 | 0.873 | -0.097 | -0.850 | -0.541 | 1816 | 4.26 | 0.551 |
| 0.50 | -0.122 | 0.087 | -0.025 | 0.884 | -0.090 | -0.846 | -0.553 | 1782 | 4.13 | 0.556 |
| 0.55 | -0.268 | -0.063 | -0.176 | 0.907 | -0.078 | -0.837 | -0.579 | 1710 | 3.82 | 0.562 |
| 0.60 | -0.401 | -0.203 | -0.314 | 0.928 | -0.069 | -0.830 | -0.602 | 1644 | 3.57 | 0.569 |
| 0.65 | -0.523 | -0.331 | -0.440 | 0.946 | -0.060 | -0.823 | -0.622 | 1592 | 3.36 | 0.575 |
| 0.70 | -0.634 | -0.452 | -0.555 | 0.962 | -0.053 | -0.818 | -0.639 | 1545 | 3.20 | 0.582 |
| 0.75 | -0.737 | -0.562 | -0.661 | 0.979 | -0.046 | -0,813 | -0.653 | 1507 | 3.07 | 0.587 |
| 0.80 | -0.829 | -0.666 | -0.760 | 0.992 | -0.041 | -0.809 | -0.666 | 1476 | 2.98 | 0.593 |
| 0.85 | -0.915 | -0.761 | -0.851 | 1.006 | -0.037 | -0.805 | -0.676 | 1452 | 2.92 | 0.598 |
| 0.90 | -0.993 | -0.848 | -0.933 | 1.018 | -0.035 | -0.802 | -0.685 | 1432 | 2.89 | 0.604 |
| 0.95 | -1.066 | -0.932 | -1.010 | 1.027 | -0.032 | -0.800 | -0.692 | 1416 | 2.88 | 0.609 |
| 1.00 | -1.133 | -1.009 | -1.080 | 1.036 | -0.032 | -0.798 | -0.698 | 1406 | 2.90 | 0.613 |
| 1.10 | -1.249 | -1.145 | -1.208 | 1.052 | -0.030 | -0.795 | -0.706 | 1396 | 2.99 | 0.622 |
| 1.20 | -1.345 | -1.265 | -1.315 | 1.064 | -0.032 | -0.794 | -0.710 | 1400 | 3.14 | 0.629 |
| 1.30 | -1.428 | -1.370 | -1.407 | 1.073 | -0.035 | -0.793 | -0.711 | 1416 | 3.36 | 0.637 |
| 1.40 | -1.495 | -1.460 | -1.483 | 1.080 | -0.039 | -0.794 | -0.709 | 1442 | 3.62 | 0.643 |
| 1.50 | -1.552 | -1.538 | -1.550 | 1.085 | -0.044 | -0.796 | -0.704 | 1479 | 3.92 | 0.649 |
| 1.60 | -1.598 | -1.608 | -1.605 | 1.087 | -0.051 | -0.798 | -0.697 | 1524 | 4.26 | 0.654 |
| 1.70 | -1.634 | -1.668 | -1.652 | 1.089 | -0.058 | -0.801 | -0.689 | 1581 | 4.62 | 0.660 |
| 1.80 | -1.663 | -1.718 | -1.689 | 1.087 | -0.067 | -0.804 | -0.679 | 1644 | 5.01 | 0.664 |
| 1.90 | -1.685 | -1.763 | -1.720 | 1.087 | -0.074 | -0.808 | -0.667 | 1714 | 5.42 | 0.669 |
| 2.00 | -1.699 | -1.801 | -1.743 | 1.085 | -0.085 | -0.812 | -0.655 | 1795 | 5.85 | 0.672 |

1.3 ATTENUATION RELATIONSHIPS DERIVED BY CAMPBELL (1997)

The following equations were derived by Campbell for the median value of peak horizontal acceleration (in g's) and the median value of horizontal spectral ordinates (in g's) for 5% spectral damping:

|  | [1-10] |
| --- | --- |

|  | [1-11] |
| --- | --- |

In these equations,  is moment magnitude, and the source-to-site distance, , is the shortest distance between the recording site and the assumed zone of seismogenic rupture on the fault.  Campbell indicates, based on the work of Marone and Scholz (1988), that the upper 2 to 4 km of the fault zone is typically non-seismogenic.  The style of faulting variable, , is equal to zero for strike slip faulting and is equal to unity for all other style of faulting.  The parameters  and  define the local site conditions as follows:

for soft rock sites; and

for hard rock sites.

The parameter  is depth to basement rock below the site.  The function  is given by:

|  | [1-12] |
| --- | --- |

The values of the coefficients  are provided in Table 1-4.

Campbell derived relationships for the standard error of estimate of  as a function of mean predicted value of  and mean earthquake magnitude.  Thus:

|  | [1-13] |
| --- | --- |

|  | [1-14] |
| --- | --- |

Campbell suggests that Eq. 1-13 is more statistically robust than Eq. 1-14.

Table 1-4

Coefficients Derived by Campbell (1997)

| Period |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.05 | 0.05 | 0 | 0 | -0.0011 | 0.000055 | 0.20 | 0 | 0 |
| 0.075 | 0.27 | 0 | 0 | -0.0024 | 0.000095 | 0.22 | 0 | 0 |
| 0.1 | 0.48 | 0 | 0 | -0.0024 | 0.000007 | 0.14 | 0 | 0 |
| 0.15 | 0.72 | 0 | 0 | -0.0010 | -0.00027 | -0.02 | 0 | 0 |
| 0.2 | 0.79 | 0 | 0 | 0.0011 | -0.00053 | -0.18 | 0 | 0 |
| 0.3 | 0.77 | 0 | 0 | 0.0035 | -0.00072 | -0.40 | 0 | 0 |
| 0.5 | -0.28 | 0.74 | 0.66 | 0.0068 | -0.001 | -0.42 | 0.25 | 0.62 |
| 0.75 | -1.08 | 1.23 | 0.66 | 0.0077 | -0.001 | -0.44 | 0.37 | 0.62 |
| 1 | -1.79 | 1.59 | 0.66 | 0.0085 | -0.001 | -0.38 | 0.57 | 0.62 |
| 1.5 | -2.65 | 1.98 | 0.66 | 0.0094 | -0.001 | -0.32 | 0.72 | 0.62 |
| 2 | -3.28 | 2.23 | 0.66 | 0.0100 | -0.001 | -0.36 | 0.83 | 0.62 |
| 3 | -4.07 | 2.39 | 0.66 | 0.0108 | -0.001 | -0.22 | 0.86 | 0.62 |
| 4 | -4.26 | 2.03 | 0.66 | 0.0112 | -0.001 | -0.30 | 1.05 | 0.62 |

1.4 ATTENUATION RELATIONSHIPS DERIVED BY IDRISS (2002)

The following equation was derived by Idriss for spectral ordinates at rock sites:

|  | [1-15] |
| --- | --- |

is the median spectral acceleration in g (5% damping), or peak ground acceleration (pga), in g's,  is moment magnitude,  is the closest distance to the rupture plane in km,  is the fault type (1 for reverse and reverse/oblique, and 0 otherwise), and  are coefficients, whose values are listed in Table 1-5a, 1-5b; and 1-5c.  Table 5a provides values of these coefficients for .  Values for  are listed in Table 5b, and those for  in table 5c.

Standard error terms are obtained using the following expressions:

|  | [1-16] |
| --- | --- |

The values of  and  are listed in Table 1-6.

Table 1-5a Coefficients for the Median Spectral Ordinates Using Equations

Derived by Idriss (2002) for

| Period - sec |  |  |  |  |
| --- | --- | --- | --- | --- |
| 0.01 | 2.5030 | 0.1337 | 2.8008 | -0.1970 |
| 0.03 | 2.5030 | 0.1337 | 2.8008 | -0.1970 |
| 0.04 | 2.9873 | 0.0290 | 2.7850 | -0.2081 |
| 0.05 | 3.2201 | 0.0099 | 2.7802 | -0.2092 |
| 0.06 | 3.2988 | 0.0187 | 2.7784 | -0.2083 |
| 0.07 | 3.2935 | 0.0378 | 2.7777 | -0.2072 |
| 0.075 | 3.2702 | 0.0489 | 2.7774 | -0.2068 |
| 0.08 | 3.2381 | 0.0606 | 2.7773 | -0.2065 |
| 0.09 | 3.1522 | 0.0845 | 2.7770 | -0.2061 |
| 0.1 | 3.0467 | 0.1083 | 2.7767 | -0.2060 |
| 0.11 | 2.9308 | 0.1316 | 2.7763 | -0.2061 |
| 0.12 | 2.8093 | 0.1541 | 2.7759 | -0.2063 |
| 0.13 | 2.6859 | 0.1758 | 2.7754 | -0.2066 |
| 0.14 | 2.5579 | 0.1966 | 2.7748 | -0.2070 |
| 0.15 | 2.4301 | 0.2166 | 2.7741 | -0.2074 |
| 0.16 | 2.3026 | 0.2357 | 2.7733 | -0.2079 |
| 0.17 | 2.1785 | 0.2541 | 2.7724 | -0.2083 |
| 0.18 | 2.0543 | 0.2718 | 2.7714 | -0.2088 |
| 0.19 | 1.9324 | 0.2888 | 2.7704 | -0.2092 |
| 0.2 | 1.8129 | 0.3051 | 2.7693 | -0.2096 |
| 0.22 | 1.5794 | 0.3360 | 2.7668 | -0.2105 |
| 0.24 | 1.3575 | 0.3646 | 2.7641 | -0.2112 |
| 0.25 | 1.2490 | 0.3782 | 2.7626 | -0.2116 |
| 0.26 | 1.1435 | 0.3913 | 2.7611 | -0.2119 |
| 0.28 | 0.9381 | 0.4161 | 2.7580 | -0.2126 |
| 0.3 | 0.7437 | 0.4394 | 2.7548 | -0.2132 |
| 0.32 | 0.5553 | 0.4612 | 2.7514 | -0.2137 |
| 0.34 | 0.3755 | 0.4816 | 2.7480 | -0.2143 |
| 0.35 | 0.2883 | 0.4914 | 2.7462 | -0.2145 |
| 0.36 | 0.2049 | 0.5008 | 2.7445 | -0.2147 |
| 0.38 | 0.0362 | 0.5190 | 2.7410 | -0.2152 |
| 0.4 | -0.1223 | 0.5361 | 2.7374 | -0.2156 |
| 0.45 | -0.4985 | 0.5749 | 2.7285 | -0.2167 |
| 0.5 | -0.8415 | 0.6091 | 2.7197 | -0.2176 |
| 0.55 | -1.1581 | 0.6393 | 2.7112 | -0.2185 |
| 0.6 | -1.7051 | 0.7087 | 2.7030 | -0.2194 |
| 0.7 | -1.9821 | 0.7127 | 2.6878 | -0.2211 |
| 0.8 | -2.4510 | 0.7514 | 2.6742 | -0.2228 |
| 0.9 | -2.8715 | 0.7847 | 2.6624 | -0.2244 |
| 1 | -3.2511 | 0.8139 | 2.6522 | -0.2259 |
| 1.5 | -4.7813 | 0.9288 | 2.6206 | -0.2326 |
| 2 | -5.9481 | 1.0246 | 2.6097 | -0.2368 |
| 3 | -7.7976 | 1.2121 | 2.6086 | -0.2385 |
| 4 | -9.3398 | 1.4047 | 2.6012 | -0.2336 |
| 5 | -10.7364 | 1.5973 | 2.5703 | -0.2250 |

Table 1-5b Coefficients for the Median Spectral Ordinates Using Equations

Derived by Idriss (2002) for

| Period - sec |  |  |  |  |
| --- | --- | --- | --- | --- |
| 0.01 | 4.3387 | -0.1754 | 3.2564 | -0.2739 |
| 0.03 | 4.3387 | -0.1754 | 3.2564 | -0.2739 |
| 0.04 | 3.9748 | -0.1244 | 3.0378 | -0.2468 |
| 0.05 | 3.9125 | -0.0972 | 2.9689 | -0.2381 |
| 0.06 | 3.8984 | -0.0777 | 2.9481 | -0.2355 |
| 0.07 | 3.8852 | -0.0613 | 2.9448 | -0.2352 |
| 0.075 | 3.8748 | -0.0536 | 2.9458 | -0.2354 |
| 0.08 | 3.8613 | -0.0462 | 2.9477 | -0.2358 |
| 0.09 | 3.8249 | -0.0319 | 2.9527 | -0.2367 |
| 0.1 | 3.7774 | -0.0181 | 2.9578 | -0.2376 |
| 0.11 | 3.7206 | -0.0046 | 2.9623 | -0.2385 |
| 0.12 | 3.6562 | 0.0086 | 2.9659 | -0.2393 |
| 0.13 | 3.5860 | 0.0215 | 2.9685 | -0.2401 |
| 0.14 | 3.5111 | 0.0341 | 2.9703 | -0.2407 |
| 0.15 | 3.4327 | 0.0464 | 2.9712 | -0.2412 |
| 0.16 | 3.3515 | 0.0586 | 2.9713 | -0.2416 |
| 0.17 | 3.2683 | 0.0704 | 2.9708 | -0.2420 |
| 0.18 | 3.1837 | 0.0821 | 2.9697 | -0.2423 |
| 0.19 | 3.0980 | 0.0934 | 2.9681 | -0.2425 |
| 0.2 | 3.0117 | 0.1046 | 2.9660 | -0.2426 |
| 0.22 | 2.8382 | 0.1263 | 2.9608 | -0.2428 |
| 0.24 | 2.6648 | 0.1471 | 2.9544 | -0.2428 |
| 0.25 | 2.5786 | 0.1572 | 2.9509 | -0.2428 |
| 0.26 | 2.4929 | 0.1671 | 2.9472 | -0.2427 |
| 0.28 | 2.3231 | 0.1863 | 2.9393 | -0.2425 |
| 0.3 | 2.1559 | 0.2049 | 2.9310 | -0.2423 |
| 0.32 | 1.9916 | 0.2228 | 2.9224 | -0.2419 |
| 0.34 | 1.8306 | 0.2400 | 2.9135 | -0.2416 |
| 0.35 | 1.7512 | 0.2484 | 2.9091 | -0.2414 |
| 0.36 | 1.6728 | 0.2567 | 2.9045 | -0.2412 |
| 0.38 | 1.5183 | 0.2728 | 2.8955 | -0.2407 |
| 0.4 | 1.3671 | 0.2883 | 2.8864 | -0.2403 |
| 0.45 | 1.0036 | 0.3251 | 2.8639 | -0.2391 |
| 0.5 | 0.6598 | 0.3591 | 2.8419 | -0.2379 |
| 0.55 | 0.3347 | 0.3906 | 2.8206 | -0.2367 |
| 0.6 | 0.0271 | 0.4200 | 2.8002 | -0.2356 |
| 0.7 | -0.5407 | 0.4729 | 2.7624 | -0.2334 |
| 0.8 | -1.0522 | 0.5193 | 2.7283 | -0.2315 |
| 0.9 | -1.5147 | 0.5603 | 2.6980 | -0.2298 |
| 1 | -1.9343 | 0.5966 | 2.6712 | -0.2284 |
| 1.5 | -3.5364 | 0.7255 | 2.5803 | -0.2246 |
| 2 | -4.5538 | 0.7945 | 2.5443 | -0.2252 |
| 3 | -5.5133 | 0.8254 | 2.5790 | -0.2354 |
| 4 | -5.5624 | 0.7672 | 2.7072 | -0.2537 |
| 5 | -5.0154 | 0.6513 | 2.8979 | -0.2773 |

Table 1-5c Coefficients for the Median Spectral Ordinates Using Equations

Derived by Idriss (2002) for

| Period - sec |  |  |  |  |
| --- | --- | --- | --- | --- |
| 0.01 | 6.5668 | -0.5164 | 3.2606 | -0.2740 |
| 0.03 | 6.5668 | -0.5164 | 3.2606 | -0.2740 |
| 0.04 | 6.1747 | -0.4717 | 3.0156 | -0.2461 |
| 0.05 | 6.2734 | -0.4675 | 2.9671 | -0.2400 |
| 0.06 | 6.4228 | -0.4696 | 2.9677 | -0.2396 |
| 0.07 | 6.5418 | -0.4704 | 2.9791 | -0.2406 |
| 0.075 | 6.5828 | -0.4698 | 2.9850 | -0.2413 |
| 0.08 | 6.6162 | -0.4685 | 2.9904 | -0.2419 |
| 0.09 | 6.6541 | -0.4642 | 2.9989 | -0.2429 |
| 0.1 | 6.6594 | -0.4580 | 3.0044 | -0.2437 |
| 0.11 | 6.6436 | -0.4504 | 3.0071 | -0.2442 |
| 0.12 | 6.6084 | -0.4419 | 3.0077 | -0.2446 |
| 0.13 | 6.5639 | -0.4328 | 3.0067 | -0.2448 |
| 0.14 | 6.5085 | -0.4233 | 3.0044 | -0.2448 |
| 0.15 | 6.4448 | -0.4137 | 3.0012 | -0.2448 |
| 0.16 | 6.3778 | -0.4040 | 2.9974 | -0.2447 |
| 0.17 | 6.3077 | -0.3945 | 2.9931 | -0.2446 |
| 0.18 | 6.2366 | -0.3850 | 2.9885 | -0.2444 |
| 0.19 | 6.1623 | -0.3758 | 2.9836 | -0.2442 |
| 0.2 | 6.0872 | -0.3668 | 2.9786 | -0.2440 |
| 0.22 | 5.9380 | -0.3494 | 2.9684 | -0.2436 |
| 0.24 | 5.7915 | -0.3331 | 2.9580 | -0.2431 |
| 0.25 | 5.7213 | -0.3253 | 2.9529 | -0.2428 |
| 0.26 | 5.6485 | -0.3178 | 2.9477 | -0.2426 |
| 0.28 | 5.5097 | -0.3035 | 2.9376 | -0.2421 |
| 0.3 | 5.3744 | -0.2900 | 2.9276 | -0.2417 |
| 0.32 | 5.2428 | -0.2774 | 2.9178 | -0.2412 |
| 0.34 | 5.1167 | -0.2656 | 2.9082 | -0.2408 |
| 0.35 | 5.0563 | -0.2600 | 2.9034 | -0.2405 |
| 0.36 | 4.9957 | -0.2545 | 2.8987 | -0.2403 |
| 0.38 | 4.8752 | -0.2441 | 2.8894 | -0.2399 |
| 0.4 | 4.7604 | -0.2342 | 2.8803 | -0.2395 |
| 0.45 | 4.4900 | -0.2119 | 2.8581 | -0.2384 |
| 0.5 | 4.2369 | -0.1922 | 2.8367 | -0.2374 |
| 0.55 | 4.0027 | -0.1747 | 2.8160 | -0.2363 |
| 0.6 | 3.7826 | -0.1589 | 2.7960 | -0.2353 |
| 0.7 | 3.3750 | -0.1314 | 2.7580 | -0.2333 |
| 0.8 | 3.0078 | -0.1078 | 2.7227 | -0.2314 |
| 0.9 | 2.6734 | -0.0870 | 2.6901 | -0.2295 |
| 1 | 2.3648 | -0.0683 | 2.6603 | -0.2278 |
| 1.5 | 1.1109 | 0.0068 | 2.5501 | -0.2211 |
| 2 | 0.1818 | 0.0649 | 2.4928 | -0.2176 |
| 3 | -1.1016 | 0.1532 | 2.4711 | -0.2168 |
| 4 | -1.9306 | 0.2153 | 2.4953 | -0.2190 |
| 5 | -2.5042 | 0.2579 | 2.5107 | -0.2199 |

Table 1-6 Style of Faulting and Standard Error Coefficients for Spectral Ordinates

Using Equations Derived by Idriss (2002)

| Period - sec |  |  |  |  |
| --- | --- | --- | --- | --- |
| 0.01 | 0.320 | 0.720 | 1.320 | 0.450 |
| 0.03 | 0.320 | 0.720 | 1.320 | 0.450 |
| 0.04 | 0.320 | 0.720 | 1.320 | 0.450 |
| 0.05 | 0.320 | 0.720 | 1.320 | 0.450 |
| 0.06 | 0.320 | 0.730 | 1.330 | 0.460 |
| 0.07 | 0.320 | 0.739 | 1.339 | 0.469 |
| 0.075 | 0.320 | 0.743 | 1.343 | 0.473 |
| 0.08 | 0.320 | 0.747 | 1.347 | 0.477 |
| 0.09 | 0.320 | 0.753 | 1.353 | 0.483 |
| 0.1 | 0.320 | 0.760 | 1.360 | 0.490 |
| 0.11 | 0.324 | 0.765 | 1.365 | 0.495 |
| 0.12 | 0.327 | 0.770 | 1.370 | 0.500 |
| 0.13 | 0.330 | 0.775 | 1.375 | 0.505 |
| 0.14 | 0.332 | 0.779 | 1.379 | 0.509 |
| 0.15 | 0.335 | 0.783 | 1.383 | 0.513 |
| 0.16 | 0.337 | 0.787 | 1.387 | 0.517 |
| 0.17 | 0.339 | 0.791 | 1.391 | 0.521 |
| 0.18 | 0.341 | 0.794 | 1.394 | 0.524 |
| 0.19 | 0.343 | 0.797 | 1.397 | 0.527 |
| 0.2 | 0.345 | 0.800 | 1.400 | 0.530 |
| 0.22 | 0.348 | 0.806 | 1.406 | 0.536 |
| 0.24 | 0.352 | 0.811 | 1.411 | 0.541 |
| 0.25 | 0.353 | 0.814 | 1.414 | 0.544 |
| 0.26 | 0.355 | 0.816 | 1.416 | 0.546 |
| 0.28 | 0.357 | 0.820 | 1.420 | 0.550 |
| 0.3 | 0.360 | 0.825 | 1.425 | 0.555 |
| 0.32 | 0.360 | 0.829 | 1.429 | 0.559 |
| 0.34 | 0.360 | 0.832 | 1.432 | 0.562 |
| 0.35 | 0.360 | 0.834 | 1.434 | 0.564 |
| 0.36 | 0.360 | 0.836 | 1.436 | 0.566 |
| 0.38 | 0.360 | 0.839 | 1.439 | 0.569 |
| 0.4 | 0.360 | 0.842 | 1.442 | 0.572 |
| 0.45 | 0.360 | 0.849 | 1.449 | 0.579 |
| 0.5 | 0.360 | 0.856 | 1.456 | 0.586 |
| 0.55 | 0.350 | 0.862 | 1.462 | 0.592 |
| 0.6 | 0.340 | 0.867 | 1.467 | 0.597 |
| 0.7 | 0.322 | 0.877 | 1.477 | 0.607 |
| 0.8 | 0.307 | 0.885 | 1.485 | 0.615 |
| 0.9 | 0.294 | 0.893 | 1.493 | 0.623 |
| 1 | 0.282 | 0.900 | 1.500 | 0.630 |
| 1.5 | 0.236 | 0.900 | 1.500 | 0.630 |
| 2 | 0.204 | 0.900 | 1.500 | 0.630 |
| 3 | 0.158 | 0.900 | 1.500 | 0.630 |
| 4 | 0.125 | 0.900 | 1.500 | 0.630 |
| 5 | 0.100 | 0.900 | 1.500 | 0.630 |

1.5 ATTENUATION RELATIONSHIPS DERIVED BY SADIGH, CHANG, EGAN, MAKDISI, AND YOUNGS (1997)

The following equation was derived by Sadigh et al for spectral ordinates at rock sites:

|  | [1-17] |
| --- | --- |

is the median spectral acceleration in g (5% damping), or peak ground acceleration (pga), in g's,  is moment magnitude,  is the closest distance to the rupture plane in km, and  are coefficients.  The values of the standard error terms are listed in Table 1-7.  The values of the coefficients  are provided in Table 1-8.

Table 1-7 Coefficients for Standard Error Terms Using

Equations Derived by Sadigh et al (1997)

| Period - sec | Standard Error Term | Minimum Value for |
| --- | --- | --- |
| zpa |  | 0.38 |
| 0.07 |  | 0.39 |
| 0.10 |  | 0.40 |
| 0.20 |  | 0.42 |
| 0.30 |  | 0.44 |
| 0.40 |  | 0.47 |
| 0.50 |  | 0.49 |
| 0.75 |  | 0.51 |
| ≥1.00 |  | 0.52 |

Table 1-8 Coefficients for the Median Spectral Ordinates Using Equations

Derived by Sadigh et al (1997)

| Period |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| zpa | -0.624 | 1 | 0.000 | -2.100 | 1.29649 | 0.250 | 0.000 |
| 0.03 | -0.624 | 1 | 0.000 | -2.100 | 1.29649 | 0.250 | 0.000 |
| 0.07 | 0.110 | 1 | 0.006 | -2.128 | 1.29649 | 0.250 | -0.082 |
| 0.1 | 0.275 | 1 | 0.006 | -2.148 | 1.29649 | 0.250 | -0.041 |
| 0.2 | 0.153 | 1 | -0.004 | -2.080 | 1.29649 | 0.250 | 0.000 |
| 0.3 | -0.057 | 1 | -0.017 | -2.028 | 1.29649 | 0.250 | 0.000 |
| 0.4 | -0.298 | 1 | -0.028 | -1.990 | 1.29649 | 0.250 | 0.000 |
| 0.5 | -0.588 | 1 | -0.040 | -1.945 | 1.29649 | 0.250 | 0.000 |
| 0.75 | -1.208 | 1 | -0.050 | -1.865 | 1.29649 | 0.250 | 0.000 |
| 1 | -1.705 | 1 | -0.055 | -1.800 | 1.29649 | 0.250 | 0.000 |
| 1.5 | -2.407 | 1 | -0.065 | -1.725 | 1.29649 | 0.250 | 0.000 |
| 2 | -2.945 | 1 | -0.070 | -1.670 | 1.29649 | 0.250 | 0.000 |
| 3 | -3.700 | 1 | -0.080 | -1.610 | 1.29649 | 0.250 | 0.000 |
| 4 | -4.230 | 1 | -0.100 | -1.570 | 1.29649 | 0.250 | 0.000 |
| zpa | -1.237 | 1.1 | 0.000 | -2.100 | -0.48451 | 0.524 | 0.000 |
| 0.03 | -1.237 | 1.1 | 0.000 | -2.100 | -0.48451 | 0.524 | 0.000 |
| 0.07 | -0.540 | 1.1 | 0.006 | -2.128 | -0.48451 | 0.524 | -0.082 |
| 0.1 | -0.375 | 1.1 | 0.006 | -2.148 | -0.48451 | 0.524 | -0.041 |
| 0.2 | -0.497 | 1.1 | -0.004 | -2.080 | -0.48451 | 0.524 | 0.000 |
| 0.3 | -0.707 | 1.1 | -0.017 | -2.028 | -0.48451 | 0.524 | 0.000 |
| 0.4 | -0.948 | 1.1 | -0.028 | -1.990 | -0.48451 | 0.524 | 0.000 |
| 0.5 | -1.238 | 1.1 | -0.040 | -1.945 | -0.48451 | 0.524 | 0.000 |
| 0.75 | -1.858 | 1.1 | -0.050 | -1.865 | -0.48451 | 0.524 | 0.000 |
| 1 | -2.355 | 1.1 | -0.055 | -1.800 | -0.48451 | 0.524 | 0.000 |
| 1.5 | -3.057 | 1.1 | -0.065 | -1.725 | -0.48451 | 0.524 | 0.000 |
| 2 | -3.595 | 1.1 | -0.070 | -1.670 | -0.48451 | 0.524 | 0.000 |
| 3 | -4.350 | 1.1 | -0.080 | -1.610 | -0.48451 | 0.524 | 0.000 |
| 4 | -4.880 | 1.1 | -0.100 | -1.570 | -0.48451 | 0.524 | 0.000 |

Note that the above coefficients are applicable to ground motions generated by a strike slip event.  Sadigh et al suggest that the calculated spectral ordinates be multiplied by a factor of 1.2 for reverse / thrust events.

ATTACHMENT 2

ATTENUATION RELATIONSHIPS FOR MOTIONS

IN EASTERN NORTH AMERICA (ENA)

The attenuation relationships derived by Toro et al (1997) and those by Atkinson & Boore (1997) are summarized in this Attachment.

2.1 ATTENUATION RELATIONSHIPS BY TORO, ABRAHAMSON AND SCHNEIDER (1997)

The functional form adopted by Toro et al is the following:

|  | [2-1] |
| --- | --- |

|  | [2-2] |
| --- | --- |

in which,  is the median spectral acceleration in g (5% damping) or peak ground acceleration (pga) in g's,  is either  magnitude  or moment magnitude ,  through  are coefficients that depend on the frequency and on the region under consideration, and  is the closest horizontal distance to the rupture surface if this surface is projected to the ground surface (i.e., the Joyner-Boore distance) in km.

Two regions were considered by Toro et al (1997) in deriving attenuation relationships for Eastern North America (ENA), namely the Mid-Continent and the Gulf Crustal Regions.  The extent of each region is depicted in Fig. 2-1.  The coefficients  for various frequencies and for zpa and applicable to each region are listed in Table 2-1 for equations using moment magnitude and for equations using  magnitude.

2.2 ATTENUATION RELATIONSHIPS BY ATKINSON AND BOORE (1997)

The following functional form was used by Atkinson & Bore (1997) to calculate the median spectral acceleration

|  | [2-3] |
| --- | --- |

in which,  is the median spectral acceleration in g (5% damping) or peak ground acceleration (pga) in g's,  is moment magnitude  through  are coefficients that depend on frequency, and  is the hypocentral distance in km.  The coefficients  for various frequencies and for pga are listed in Table 2-2.

Table 2-1 Coefficients of Attenuation Equations Derived by Toro et al (1997)

| Frequency (Hz) | Coefficient |
| --- | --- |
| Mid-Continent Region – Equations Using Moment Magnitude |
| 0.5 | -0.74 | 1.86 | -0.31 | 0.92 | 0.46 | 0.0017 | 6.9 |
| 1 | 0.09 | 1.42 | -0.20 | 0.90 | 0.49 | 0.0023 | 6.8 |
| 2.5 | 1.07 | 1.05 | -0.10 | 0.93 | 0.56 | 0.0033 | 7.1 |
| 5 | 1.73 | 0.84 | 0 | 0.98 | 0.66 | 0.0042 | 7.5 |
| 10 | 2.37 | 0.81 | 0 | 1.10 | 1.02 | 0.0040 | 8.3 |
| 25 | 3.68 | 0.80 | 0 | 1.46 | 1.77 | 0.0013 | 10.5 |
| 35 | 4.00 | 0.79 | 0 | 1.57 | 1.83 | 0.0008 | 11.1 |
| pga | 2.20 | 0.81 | 0 | 1.27 | 1.16 | 0.0021 | 9.3 |
| Mid-Continent Region – Equations Using Magnitude |
| 0.5 | -0.97 | 2.52 | -0.47 | 0.93 | 0.60 | 0.0012 | 7.0 |
| 1 | -0.12 | 2.05 | -0.34 | 0.90 | 0.59 | 0.0019 | 6.8 |
| 2.5 | 0.90 | 1.70 | -0.26 | 0.94 | 0.65 | 0.0030 | 7.2 |
| 5 | 1.60 | 1.24 | 0 | 0.98 | 0.74 | 0.0039 | 7.5 |
| 10 | 2.36 | 1.23 | 0 | 1.12 | 1.05 | 0.0043 | 8.5 |
| 25 | 3.54 | 1.19 | 0 | 1.46 | 1.84 | 0.0010 | 10.5 |
| 35 | 3.87 | 1.19 | 0 | 1.58 | 1.90 | 0.0005 | 11.1 |
| pga | 2.07 | 1.20 | 0 | 1.28 | 1.23 | 0.0018 | 9.3 |
| Gulf Region – Equations Using Moment Magnitude |
| 0.5 | -0.81 | -1.60 | -0.26 | 0.74 | 0.71 | 0.0025 | 6.6 |
| 1 | 0.24 | -0.60 | -0.15 | 0.79 | 0.82 | 0.0034 | 7.2 |
| 2.5 | 1.64 | 0.80 | -0.08 | 0.99 | 1.27 | 0.0036 | 8.9 |
| 5 | 3.10 | 2.26 | 0 | 1.34 | 1.95 | 0.0017 | 11.4 |
| 10 | 5.08 | 4.25 | 0 | 1.87 | 2.52 | 0.0002 | 14.1 |
| 25 | 5.19 | 4.35 | 0 | 1.96 | 1.96 | 0.0004 | 12.9 |
| 35 | 4.81 | 3.97 | 0 | 1.89 | 1.80 | 0.0008 | 11.9 |
| pga | 2.91 | 2.07 | 0 | 1.49 | 1.61 | 0.0014 | 10.9 |
| Gulf Region – Equations Using Magnitude |
| 0.5 | -1.01 | 2.38 | -0.42 | 0.75 | 0.83 | 0.0032 | 6.8 |
| 1 | 0.06 | 1.97 | -0.32 | 0.80 | 0.92 | 0.0030 | 7.3 |
| 2.5 | 1.49 | 1.74 | -0.26 | 1.00 | 1.36 | 0.0032 | 9.0 |
| 5 | 3.00 | 1.31 | 0 | 1.35 | 2.03 | 0.0014 | 11.4 |
| 10 | 4.65 | 1.30 | 0 | 1.78 | 2.41 | 0.0000 | 13.8 |
| 25 | 5.08 | 1.29 | 0 | 1.97 | 2.04 | 0.0000 | 12.9 |
| 35 | 4.68 | 1.30 | 0 | 1.89 | 1.88 | 0.0005 | 11.9 |
| pga | 2.80 | 1.31 | 0 | 1.49 | 1.68 | 0.0017 | 10.9 |

Table 2-2 Coefficients of Attenuation Equations Derived by Atkinson & Boore (1997)

| Frequency (Hz) | Coefficient |
| --- | --- |
| 0.5 | -1.660 | 1.460 | -0.039 | 0 |
| 0.8 | -0.900 | 1.462 | -0.071 | 0 |
| 1.0 | -0.508 | 1.428 | -0.094 | 0 |
| 1.3 | -0.094 | 1.391 | -0.118 | 0 |
| 2.0 | 0.620 | 1.267 | -0.147 | 0 |
| 3.2 | 1.265 | 1.094 | -0.165 | 0.00024 |
| 5.0 | 1.749 | 0.963 | -0.148 | 0.00105 |
| 7.9 | 2.140 | 0.864 | -0.129 | 0.00207 |
| 10 | 2.301 | 0.829 | -0.121 | 0.00279 |
| 13 | 2.463 | 0.797 | -0.113 | 0.00352 |
| 20 | 2.762 | 0.755 | -0.110 | 0.00520 |
| pga | 1.841 | 0.686 | -0.123 | 0.00311 |

Fig. 2-1 Regions Considered by Toro et al (1997) in Deriving Attenuation Relationships for Eastern North America (ENA)

ATTACHMENT 3

ATTENUATION RELATIONSHIPS FOR SUBDUCTION EARTHQUAKES

The attenuation relationships derived by Youngs et al (1997) are summarized in this Attachment.

3.1 ATTENUATION RELATIONSHIPS DERIVED BY YOUNGS, CHIOU, SILVA AND HUMPHREY (1997)

The following attenuation relationship was derived by Youngs et al (1997):

|  | [3-1] |
| --- | --- |

|  | [3-2] |
| --- | --- |

|  | [3-3] |
| --- | --- |

is spectral acceleration in g's,  is moment magnitude,  is closest distance from site to rupture surface in km,  is depth in km, and  = 0 for interface events (such as the Cascadia Zone) and  = 1 for intra-slab events (such as the Juan de Fuca).

Note that for magnitudes greater than 8, the  term for  = 8 is to be used.

The values of the coefficients  are listed in Table 3-1.

Table 3-1 Coefficients of Attenuation Equations Derived by Young et al (1997)

| Period - sec |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| 0.01 | 0 | 0 | -2.552 | 1.45 | -0.1 |
| 0.075 | 1.275 | 0 | -2.707 | 1.45 | -0.1 |
| 0.1 | 1.188 | -0.0011 | -2.655 | 1.45 | -0.1 |
| 0.2 | 0.722 | -0.0027 | -2.528 | 1.45 | -0.1 |
| 0.3 | 0.246 | -0.0036 | -2.454 | 1.45 | -0.1 |
| 0.4 | -0.115 | -0.0043 | -2.401 | 1.45 | -0.1 |
| 0.5 | -0.400 | -0.0048 | -2.360 | 1.45 | -0.1 |
| 0.75 | -1.149 | -0.0057 | -2.286 | 1.45 | -0.1 |
| 1 | -1.736 | -0.0064 | -2.234 | 1.45 | -0.1 |
| 1.5 | -2.634 | -0.0073 | -2.160 | 1.50 | -0.1 |
| 2 | -3.328 | -0.0080 | -2.107 | 1.55 | -0.1 |
| 3 | -4.511 | -0.0089 | -2.033 | 1.65 | -0.1 |